## Slide 1
Drone Swarm

## Slide 2: Outline
Introduction
Requirements for Drone Swarm
Core Algorithms Used in ZJU-Fast Swarm Formation paper
Main Goal of the Paper
Drone Swarms in Military
Conclusion

## Slide 3: Introduction
Drone swarms are groups of autonomous unmanned aerial vehicles that cooperate to achieve a common objective.
Swarm intelligence enables drones to coordinate their motion and decisions through local communication and distributed control.
Collective behavior allows the swarm to adapt to dynamic environments and continue operating despite individual drone failures.
Drone swarms are widely used in applications such as surveillance, search...

## Slide 4: Requirements for Drone Swarm
Communication
Control Algorithms
Sensing & perception
Safety & collision avoidance
Scalability & robustness

## Slide 5: Control Algorithms
Consensus-Based Control
Leader–Follower Control
Virtual Structure Control
Behavior-Based Control
Cluster-Based Control

## Slide 6: Main Techniques Used in ZJU-Fast Swarm Formation paper
The graph Laplacian is used to represent the connectivity between drones in a swarm
The differentiable Laplacian-based formation similarity metric is used to maintain the swarm formation
Optimization-based trajectory planning uses polynomial trajectories (MINCO) to generate smooth and feasible paths for drones

## Slide 7: Cont...
Obstacle Avoidance: Uses a map (voxel map library) and Euclidean Signed Distance Field (ESDF) to ensure collision-free motion
Swarm Reciprocal Collision Avoidance: Prevents collisions between drones in the swarm
Distributed Planning Architecture: Each drone plans its trajectory locally while coordinating with neighbors to achieve global swarm objectives

## Slide 8: Main Goal of the Paper
Enable drone swarms to fly in a desired formation
Avoid obstacles in dense environments
Balance formation preservation and collision avoidance
Operate in a distributed (decentralized) manner
Optimize trajectories for smoothness and dynamic feasibility

## Slide 9: Drone Swarms in Military
Cluster-Based Swarm forming
    Intra-cluster
    Inter-cluster
Task allocation
    Confuse enemy sensors
    Can quickly map an entire battlefield area
    Extending radio range for friendly forces
    Surveillance
    Low-cost and reduce risk to human soldiers

## Slide 10: Conclusion
Drone swarms offer powerful solutions for complex tasks through coordinated and collaboration.
Effective communication, sensing, and control are core to swarm intelligence and safety.
Robustness and scalability ensure reliable operation in dynamic and uncertain environments.
Efficient mission planning and energy management maximize performance and endurance.
Secure and safe coordination is essential for real-world deployment and trustworthiness.

## Slide 11
Thank you