## Slide 1: Title
Drone Swarm Formations

## Slide 2: Overview
Problem: Formation flight in dense environments
Goal: Maintain formation by avoid obstacles

## Slide 3: Contributions
A novel differentiable formation, Based on: Graph Laplacians, Measures overall formation shape, Invariant to rotation...
A distributed optimization framework that includes: Formation similarity, Obstacle avoidance, Reciprocal collision avoidance, Dynamic feasibility
Extensive real-world and simulated experiments: Swarm of 7 drones in hexagon formation, Tetrahedron formation in narrow corridor with 4 drones, and heart-shaped formation simulation with 10 drones

## Slide 4: Formation Modeling
Drones as nodes in a graph
Edges/link store inter-drone distances
Complete weighted graph
    Node 1 ——5m—— Node 2
    Node 1 ——8m—— Node 3
    Node 2 ——3m—— Node 3

## Slide 5: Common methods:
Fully Connected Graph
Neighbor-Based Graph
Formation-Based (Connect drones based on the desired formation pattern)

## Slide 6: Why This Metric is New
Captures overall formation shape
Differentiable → used in optimization
Allows shape deformation safely
  Hexagon formation
  Tetrahedron formation through corridor (ormation rotates + compresses adaptively)
  Heart-shaped 10-drone formation

## Slide 7: Map + ESDF(Euclidean Signed Distance Field)
Voxel map library
ESDF allows the optimizer to compute:
    distance to nearest obstacle
    gradients for obstacle penalty

## Slide 8: Minimum Control Effort Polynomial Trajectories
MINCO is a framework for generating smooth, feasible trajectories for drones.
Position → where you are
Velocity → how fast you're moving
Acceleration → how fast your speed is changing
Jerk → how fast your acceleration is changing

## Slide 9: Minimizes multiple cost terms:
Control effort
Timing
Obstacle avoidance
Formation similarity
Reciprocal collision avoidance
Dynamic feasibility
Uniform constraint distribution

## Slide 11: Formation Similarity
Uses the graph Laplacian metric
Measures how far the current formation is from the target shape.
Penalizes drones if the shape breaks

## Slide 12: Cont...
Reciprocal Collision Avoidance(ensures that drones avoid hitting each other)
RVO (Reciprocal Velocity Obstacles)
Predict future positions, detect if their velocity vectors will cause a crash, and compute a safe velocity region
Minimum separation constraints
∥pi​−pj​∥≥dmin​
Collision cones
Mathematical method to predict if two drones will collide in the future based on current motion

## Slide 13: Drone Swarms in Military
Can quickly map an entire battlefield area
Extending radio range for friendly forces
Border monitoring
• Wide-area surveillance
Low-cost and reduce risk to human soldiers
Spread out to avoid being easily detected
• Confuse or overload enemy sensors